## Slide 1
TITLE PAGE
SMART INDIA HACKATHON 2026
Problem Statement ID – SIH26051
Problem Statement Title – Software Based Model Development for Design of Area Specific Shelter for Thermal Comfort Maintenance
Theme – Miscellaneous
PS Category – Software
Team ID – [team ID]
Team Name (Registered on portal) – ASPIRE

## Slide 2
What the problem statement is asking us to build
• A software model that predicts shelter temperature for a chosen outdoor climate.
• A user can change shelter size, shape, orientation, openings, material and thickness.
• Real weather and solar-radiation data are used instead of fixed assumptions.
• Different designs are compared under the same ambient conditions.
• The final output recommends the combination that maintains comfort with less active heating.
Why Ladakh?
• Large day/night temperature variation.
• Strong solar resource makes passive solar gain useful.
• Heat loss through walls, roofs and openings is significant.
• Thermal mass + insulation can store daytime heat and slow night-time losses.
Core design principle
SOLAR GAIN
Capture useful winter sunlight
THERMAL MASS
Store heat and release it later
INSULATION
Reduce conductive heat loss
ORIENTATION
Use site-specific solar exposure
Three required outputs
01
Indoor temperature
T_inside(t) for the selected geometry and materials
02
Solar energy
Heat gained from incident solar radiation
03
Heat flow
Heat entering/leaving through the envelope over time
ASPIRE
@SIH Idea submission- Template
2
A climate-specific digital model for designing passive shelters in Ladakh

## Slide 3
Thermal simulation pipeline
1. CLIMATE INPUT
NASA POWER hourly temperature, solar radiation, wind
2. USER DESIGN
Dimensions, orientation, openings, materials
3. PYTHON MODEL
U-value + thermal mass + solar gain + RK4
4. ANSYS
Detailed thermal simulation, mesh + boundary conditions
5. COMPARISON
Materials, thickness, shape and orientation
6 RECOMMENDATION
Best design for comfort and low heat demand
Technology stack
Engineering
ANSYS Workbench • transient thermal • parametric studies
Scientific Python
NumPy • Pandas • RK4 solver • U/R-value • thermal mass • heat balance
Backend
Flask • Flask-CORS • REST API • JSON simulation endpoints
Frontend
HTML/CSS/JavaScript • Chart.js • Three.js • OrbitControls
Data layer
NASA POWER hourly data • material-property CSV • optional SQLite/PostgreSQL
Sensors / IoT
ESP32/Arduino • temperature • humidity • solar irradiance • wind
Deployment
Git/GitHub • Docker • cached/offline datasets for remote sites
Technical Approach
Fast computational screening + ANSYS validation + interactive visualization
ASPIRE
@SIH Idea submission- Template
3

## Slide 4
Technical feasibility
Operational feasibility
Risk & mitigation
What already works
• 1,488 hourly weather records are already available in the supplied dataset.
• Python backend already performs thermal calculations and exposes API routes.
• Material library supports multiple envelope options for comparison.
• Chart.js and Three.js already provide result visualization and 3D interaction.
Next validation step
• Create an ANSYS reference geometry.
• Match the same ambient conditions and material properties.
• Compare ANSYS temperature/heat-flux results with the fast Python model.
Why it is viable
• Most inputs are numeric and can be entered through a simple form.
• The fast model can screen many designs before expensive simulation.
• The system can work with historical data first and live sensors later.
• The architecture can be reused for other climatic regions.
Practical deployment
• Local cached weather data keeps the application usable with weak internet.
• Sensor correction can reduce the gap between satellite data and site reality.
• Saved simulation cases make material/design comparison repeatable.
Main risks
• Real shelters have infiltration, thermal bridges and workmanship effects.
• Material properties can vary with moisture and temperature.
• ANSYS accuracy depends on geometry, mesh and boundary conditions.
• A single weather point cannot represent every Ladakh micro-climate.
How we mitigate them
• Sensitivity analysis across material k, thickness and opening area.
• Field calibration when sensor data becomes available.
• Human-in-the-loop review of shortlisted designs.
• Report uncertainty instead of presenting one number as absolute truth.
FEASIBILITY SCORECARD
Software prototype
READY
Weather data
READY
Material comparison
READY
ANSYS validation
NEXT
Live sensors
FUTURE
Feasibility And Viability
Why the solution is practical — and how we will control technical and deployment risk
ASPIRE
@SIH Idea submission- Template
4

## Slide 5
Prototype thermal response
Illustrative run using the supplied Ladakh weather data. The fast model is intended for screening; ANSYS and field measurements provide validation.
Key benefits
Energy
Less dependence on active heating through better passive design.
Design
Compare material, thickness, glazing and orientation before construction.
Cost
Reduce trial-and-error physical prototyping.
Field use
Accept local sensor readings and calibrate the model.
Scale
Adapt the same framework to other climatic regions.
SUCCESS = more time in comfort band + less active energy demand
Impact And Benefits
Turn simulation results into a practical shelter-design decision
ASPIRE
@SIH Idea submission- Template
5

## Slide 6
NASA POWER
Hourly solar and meteorological data for the selected location.
https://power.larc.nasa.gov/docs/services/api/temporal/hourly/
ANSYS Workbench
Thermal simulation and engineering workflow for high-fidelity validation.
https://www.ansys.com/en-in/products/ansys-workbench
Leh Climatological Data (2011–2024)
Regional temperature and weather records.
chrome-extension://efaidnbmnnnibpcajpcglclefindmkaj/https://mausam.imd.gov.in/leh/mcdata/City.pdf
FHNW — PSH Ladakh
Research project on passive-solar heated houses in Ladakh.
https://www.researchgate.net/publication/279186605_Vernacular_Architecture_and_Climatic_Control_in_the_extreme_conditions_of_Ladakh_ASPIRE-2013
What we will demonstrate
• User changes shelter geometry and materials.
• Hourly climate data enters the model.
• Python rapidly screens candidate designs.
• ANSYS validates the shortlisted geometry.
• Graphs show indoor temperature, solar gain and heat flow.
• The system ranks designs against thermal-comfort targets.
• Future sensor integration makes the model site-specific.
THERMAL LADAKH
Passive-first • data-driven • region-specific
External references are linked above.
Research & Reference
Climate data, passive-solar research and engineering-simulation references
ASPIRE
@SIH Idea submission- Template
6
Khan (2013)
Mehta, Gajjar & Bhavsar (2024)
Thermal Comfort in Vernacular Ladakhi Dwellings
Vernacular Architecture & Climatic Control in Ladakh
https://arch.su.ac.th/images/publications/ISVS12/20-Dinal.pdf
https://www.fhnw.ch/en/engineering-environment/research-services/research/projects/passive-solar-heated-houses-psh-in-ladakh-india